## Slide 1: Cortical Surface: Thickness, Surface Area, Gyrification Analysis
Martin Styner
UNC Neuro Image Research and Analysis Laboratory

## Slide 2: Motivation Neuroimaging
Brain imaging studies in neurological disorders
  Morphometry, Connectivity  Pathology
  Schizophrenia
  Autism, Fragile-X
  MPS, Krabbe
  Normal Development, High risk offspring
  Fitness & Aging

## Slide 5
Cortical thinning
Correlation with cortical thinning

## Slide 6: Existing Methods
Cortical thickness ≠ Gray matter density
  M Chung, TMI 2007, negatively correl.
Major methods
  BrainVoyager, Goebel
    Commercialized, Brain Innovation
  CIVIT/CLASP, Evans et al (MNI)
  FreeSurfer, Fischl et al (MGH)
  CRUISE, Tosun et al (JHU,UCLA,UCSF)
  BrainVISA, Maugin

## Slide 7: Image preprocessing & Cortical surface extraction
Spatial Normalization
to stereotaxic space
Intensity Non-uniformity
Correction
Native
MR image
Tissue Classification
Cortical Surface Extraction
(CLASP algorithm)
Cortical thickness measurement
CIVIT/CLASP- MNI
Notes: Now, I talk about my second theme, cortical thickness analysis. This slide shows briefly procedure of cortical thickness measurement, it is made by Dr. Alan Evans in Montreal. Firstly, this pipeline got the raw brain image and corrected the intensity non-uniformity, because the image including intensity non-uniformity is able to get misclassifications such as thick or thin gray matter. Then, N3 program is able to correct the intensity non-uniformity. Then, Corrected image was registration to stereotaxic space. In this space, skull stripping and tissue classification was performed.
And next step, generate cortical surface. Firstly, the surface was made in white matter and gray matter interface. This white matter and gray matter interface surface expand to gray matter and CSF interface following with Laplace flow. Finally, I can measure the cortical thickness by subtracting between the vertex on outer boundary and on inner boundary. This thickness is measured in Stereotaxic space. Of course, I can obtain the native cortical thickness using inverse matrix.

## Slide 8: FreeSurfer
Similar preprocessing
  Different order of steps
WM from segmentation and topology correction
GM surface from evolution along T1 intensity gradient

## Slide 9: FreeSurfer intro slides

## Slide 10: FreeSurfer Correspondence
Sulcal depth
Surface registration
to atlas

## Slide 11: CRUISE Correspondence
Koenderink Shape Measures

## Slide 12: Group-wise Correspondence
Template free
Correspondence over all surfaces
Two software packages
  ShapeWorks: Oguz & Cates
  Groups: Ilwoo Lyu

## Slide 13: Our plan
Conte/Twin/Working Memory projects
Ages 4-adult
FreeSurfer style processing
  Hack to inject our data into FS pipeline
Processing done
  Skull stripping
  Tissue and subcortical segmentation

## Slide 14: FreeSurfer Run Slides